## Slide 1
TYPE | LETTER | PIN 1 | PIN 2 | PIN 3 | PIN 4 | PIN 5 | PIN 6 | PIN 7 | PIN 8 | PIN 9 | PIN 10
3 GPIO | X | +3.3V | +5V | GPIO! | GPIO | GPIO | [UN] | [UN] | [UN] | [UN] | GND
7 GPIO | Y | +3.3V | +5V | GPIO! | GPIO | GPIO | GPIO | GPIO | GPIO | GPIO | GND
Analog In | A | +3.3V | +5V | AIN (G!) | AIN (G) | AIN | GPIO | [UN] | [UN] | [UN] | GND
CAN | C | +3.3V | +5V | GPIO! | TD (G) | RD (G) | GPIO | [UN] | [UN] | [UN] | GND
USB Device | D | +3.3V | +5V | GPIO! | D- | D+ | GPIO | GPIO | [UN] | [UN] | GND
Ethernet | E | +3.3V | +5V | [UN] | LED1 (OPT) | LED2 (OPT) | TX D- | TX D+ | RX D- | RX D+ | GND
SD Card | F | +3.3V | +5V | GPIO! | DAT0 | DAT1 | CMD | DAT2 | DAT3 | CLK | GND
USB Host | H | +3.3V | +5V | GPIO! | D- | D+ | [UN] | [UN] | [UN] | [UN] | GND
I²C | I | +3.3V | +5V | GPIO! | [UN] | [UN] | GPIO | [UN] | SDA | SCL | GND
UART+Handshaking | K | +3.3V | +5V | GPIO! | TX (G) | RX (G) | RTS | CTS | [UN] | [UN] | GND
Analog Out | O | +3.3V | +5V | GPIO! | GPIO | AOUT | [UN] | [UN] | [UN] | [UN] | GND
PWM | P | +3.3V | +5V | GPIO! | [UN] | [UN] | GPIO | PWM (G) | PWM (G) | PWM | GND
SPI | S | +3.3V | +5V | GPIO! | GPIO | GPIO | GPIO | MOSI | MISO | SCK | GND
Touch | T | +3.3V | +5V | [UN] | YU | XL | YD | XR | [UN] | [UN] | GND
UART | U | +3.3V | +5V | GPIO! | TX (G) | RX (G) | GPIO | [UN] | [UN] | [UN] | GND
LCD 1 | R | +3.3V | +5V | LCD R0 | LCD R1 | LCD R2 | LCD R3 | LCD R4 | LCD VSYNC | LCD HSYNC | GND
LCD 2 | G | +3.3V | +5V | LCD G0 | LCD G1 | LCD G2 | LCD G3 | LCD G4 | LCD G5 | BACKLIGHT | GND
LCD 3 | B | +3.3V | +5V | LCD B0 | LCD B1 | LCD B2 | LCD B3 | LCD B4 | LCD EN | LCD CLK | GND
Manufacturer Specific | Z | +3.3V | +5V | [MS] | [MS] | [MS] | [MS] | [MS] | [MS] | [MS] | GND
DaisyLink Downstream* | * | +3.3V | +5V | GPIO! | GPIO | GPIO | [MS] | [MS] | [MS] | [MS] | GND
Socket Type Definition (Version 17)
GPIO | A general-purpose digital input/output pin, operating at 3.3 Volts.
(G) | In addition to another functionality, a pin that is also usable as a GPIO.
(OPT) | A socket type that is optionally supported by a mainboard or a module.
[UN] | Modules must not connect to this pin if using this socket type. Mainboards can support multiple socket types on one socket, as long as individual pin functionalities overlap in a compatible manner. A pin from one socket type can overlap with a [UN] pin of another.
[MS] | A manufacturer-specific pin. See the documentation from the manufacturer of the board.
! | Interrupt-capable and software pull-up capable GPIO (the pull-up is switchable and in the range of 10,000 to 100,000 Ω).
* | Socket type * should not appear on a mainboard, only on DaisyLink modules. The [MS] pins on this socket type can optionally support reflashing the firmware on the module.

## Slide 2
NOTES:
All pins must be at least 3.6V tolerant.
The low logic input is 0V minimum, 0.4V maximum. Logic input high is 0.7*Vdd min, Vdd+0.2 maximum.
A module must not assume that the mainboard can pull up or pull down GPIOs using built in pull-ups/pull-downs. If a pull-up or pull-down resistor is required on a GPIO, the module should incorporate it into the PCB.
A module's screen printing must list both X and Y if it is compatible with both (the mainboard will say only “X” or ”Y,” but not both). Socket-compatibility labels are case sensitive.
If pins are shared across multiple sockets, users of shared bus socket types (such as I or S) must not impede use by other devices. For example, type S modules must respect the chip select signal.
For socket type I, mainboards should include I²C bus pull-ups of 2,200 Ω on both SDA and SCL pins. Modules must not include pull-ups on these lines.
For the DaisyLink protocol, which uses socket type X, pull ups should not be on the mainboard. For details of module pull-up requirements, see the DaisyLink specification.
For socket types C, K, and U, the rationale for having GPIO-capable function pins is to allow module makers to implement transmit-only or receive-only modules with the flexibility of an additional GPIO pin.
For socket type A and P, the rationale for having two of the three function pins with (G) and one without (G) is to allow modules to use 1, 2, or 3 Analog Input / PWM pins, and have the flexibility of GPIOs for other pins.
For DaisyLink modules (using type X), pin 3 is for the DaisyLink neighbor bus, pin 4 is used for I²C SDA, pin 5 is used for I²C SCL. See the DaisyLink spec for more details.
Note for UART ‘U’ and UART+Handshaking ‘K’ socket types: TX (Pin 3) is data from the Mainboard to the Module, and RX (Pin 4) is data from the Module to the Mainboard. These are idle high (3.3V). RTS (Pin 6) is an output from the Mainboard to the Module indicating that the module may send data, and CTS (Pin 7) is an output from the Module to the Mainboard indicating that the Mainboard may send data. RTS/CTS lines are “not ready” if high (3.3V) and “ready” if low (0V).